## Slide 1
Basic electrical engineering concepts
Eduardo Prieto
Electrical Engineering Department
CITCEA-UPC

## Slide 2: AC and DC current
DC (Direct Current)
  Less losses
  No distance limitation
  No reactive power
  More complex to change the voltage levels Power electronics required
  More complex breakers (no zero crossing currents)
AC (Alternating current)
  Three-phase allows to generate a rotating magnetic field in electrical machines, enabling ‘simple’ generation.
  Simple voltage change (step-up/step-down) - Transformers
  ‘Simple’ breakers (zero crossing currents)
Robins & Miller “Circuit analysis theory and practice”
Main characteristics

## Slide 3: Circuit elements
Passive elements
  Linear elements
    Resistances (R), inductances (L), capacitors (C)
    Lumped constants, passive elements connected using conductors.
    Distributed constants (electrical lines)
  Non-linear elements: semiconductors (power electronics), magnetic circuits (non-linear hystheresis)
Active elements:
  Energy sources
    Voltage sources
    Current sources
Basic elements

## Slide 4: Passive elements
Resistance R
Inductance L
  Equivalent to a conductor in steady state (DC)
Capacitor C
  Equivalent to an open circuit in steady state (DC)
Robins & Miller “Circuit analysis theory and practice”
Resistances, inductances and capacitors

## Slide 5: Main electrical sources
Voltage source
  Ideal
  Real (series impedance)
  Critical situation: short-circuit Max current
Current source
  Ideals
  Reals (Parallel impedance)
  Critical situation: open circuit Max voltage
Robins & Miller “Circuit analysis theory and practice”
Voltage and current

## Slide 6: Equipment - Measurements
Voltage measurement
  Parallel connection
  High impedance, ideally infinite.
Robins & Miller “Circuit analysis theory and practice”
Voltage and current measurements
Current measurement
  Series connection
  Reduced impedance, ideally 0.

## Slide 7: Kirchoff Law’s
Kirchoff Circuit Laws (KCL) – The sum of the currents entering a node has to be equal to the sum of the output currents
Kirchoff voltage law (KVL) – The sum of the voltages in a closed circuit has to be equal to 0.
Then, the sum of all the powers in a circuit has to accomplish:
Wait... we will explain later P and Q !!!
Kirchoff circuit and voltage laws
Hayt “Engineering circuit analysis”

## Slide 8: Superposition principle
If several simultaneous excitations are applied to the same network (either voltage or current sources), the global response is equal to the superposition of the partial results of each of the sources. (Voltage source conductor |Current sourcesopen circuit)
Robins & Miller “Circuit analysis theory and practice”
Example circuit (in DC)
Main description
+
It also works for AC currents!

## Slide 9: Activity 0
Illustrative example in DC
Simple DC circuit (superposition of 2 voltage sources)
Try it with AC!

## Slide 10: Activity I
Illustrative example in DC
Circuit 1 – Resistive circuit (DC)
Circuit 2 – Capacitive circuit (DC)
Circuit 3 – Inductive circuit (DC)
Circuit 4 – Resistive-inductive circuit (DC) - Dynamics

## Slide 11: AC voltage generation
Robins & Miller “Circuit analysis theory and practice”

## Slide 12: Analysis of AC circuits
RC circuit equations:
It is required to solve the differential equation and after observe the steady state.
We could use simulation!
See AC and DC examples
Robins & Miller “Circuit analysis theory and practice”
How to calculate
How to operate?

## Slide 13: Activity II
Illustrative example in AC – Simulations to solve differential equations
Circuit 1 – Resistive circuit (AC)
Circuit 2 – Capacitive circuit (AC)
Circuit 3 – Inductive circuit (AC)
Simulations are useful, but analytically, phasors will simplify the analysis!

## Slide 14: Root Mean Square value (RMS)
For alternating electric current, RMS value is equal to the value of the direct current that would produce the same average power dissipation in a resistive load – it is useful for power calculation in AC.
If the waveform is a pure sine wave (as in AC), the relationships between amplitudes (peak-to-peak, peak) and RMS are fixed and known, as they are for any continuous periodic wave.
For a sine wave, the relation between the peak and RMS value is:
Typically voltages are provided in RMS values
Verify this in simulation!
Definition

## Slide 15: Phasors
Concept definition
Sine wave:
Euler formula:
Combining both equations:
= = =
Then:
Graphic representation (counter-clockwise)
It can also be expressed in a simplified manner (usually with the angle expressed in degrees:
You can use everything you know about complex numbers!!!

## Slide 16: Equivalence phasors – time domain
Robins & Miller “Circuit analysis theory and practice”
Visual interpretation

## Slide 17: Phasor properties
Complex number-based operations
Sum/subtraction:
Product/division:
Power:
Complex conjugate operations:
Derivative
Complex-number based operations

## Slide 18: Phasors for RLC circuits
Resistance
Capacitor
Inductance
Main equations (deduction)

## Slide 19: Phasors for RLC circuits
Robins & Miller “Circuit analysis theory and practice”
Resistance
Capacitor
Inductance
Phasors (summary)

## Slide 20: Impedance (Z) and admitance (Y)
Sing criteria
Series association (I does not change)
Parallel association (V does not change)
Robins & Miller “Circuit analysis theory and practice”
+
-
V
I
+
-
V
I
Association and sign criteria

## Slide 21: Activity III
Illustrative example in AC – Simulations to solve differential equations
Circuit 1 – Resistive circuit (AC)
Circuit 2 – Capacitive circuit (AC)
Circuit 3 – Inductive circuit (AC)
Simulations are useful, but analytically, phasors will simplify the analysis!
See *.m file

## Slide 22: AC power calculation
·
Average power
Power factor
Apparent power
Average: P
Max:
Min:
Derivation
+

## Slide 23: AC power calculation
Power calculation (phasor domain)
·
cos(x)->Real part
Phasor-based calculation
=
)

## Slide 24: Power in AC circuits
Instantaneous power
+
-
v(t)
i(t)
Robins & Miller “Circuit analysis theory and practice”
Load
AC power

## Slide 25: AC power
Instantaneous power
Active power
represents the power flowing to the load
P its the average power to the load.
More power flows to the load than is returned from it.
  If P is zero, all power sent to the load is returned.
  If P has a positive value, power is dissipated by the load.
For this reason, P is called real power. In modern terminology, real power is also called active power.
Thus, active power is the average value of the instantaneous power, and the terms real power, active power, and average power mean the same
Reactive power
During the intervals that p is negative, power is being returned from the load. (This can only happen if the load contains reactive elements: L or C.)
The portion of power that flows into the load then back out is called reactive power.
Since it first flows one way then the other, its average value is zero; thus, reactive power contributes nothing to the average power to the load.
Although reactive power does no useful work, it cannot be ignored.
Extra current is required to create reactive power, and this current must be supplied by the source;
It should be noted that real power and reactive power do not exist as separate entities.
They are components of the power waveform. However, we are able to conceptually separate them for purposes of analysis.

## Slide 26: AC power
Robins & Miller “Circuit analysis theory and practice”
Derivation
Capacitor
Inductance
Resistance

## Slide 27: Activity III – Part II
AC power analysis
Circuit 1 – Resistive circuit (AC) – Active power
Circuit 2 – Capacitive circuit (AC) – Capacitive reactive power
Circuit 3 – Inductive circuit (AC) - Inductive reactive power
Simulations are useful, but analytically, phasors will simplify the analysis!

## Slide 28: Why three-phase AC?
Main characteristics and advantages
  Single-phase AC system – two conductors (phase + neutral)
  Three-phase AC power supply – three conductors (abc phases). Possible four wires if neutral is available.
  Main advantages of three-phase systems over single phase systems:
    Increased power transfer capacity. With 1,5 more cables (from 2 to 3), three times more power can be transferred.
    The power transferred is constant (for balanced systems and loads). Single phase systems show a pulsating power. This is specially relevant in mechanical devices as it can be transferred as torque oscillations.
  Three-phase systems can produce a rotating magnetic field with a specified direction and constant magnitude, which simplifies the design of electric motors, as no starting circuit is required.

## Slide 29: Three-phase systems
If we interconnect two single-phase circuits and interconnect them, which current I will be established?
Rull, Galceran, Gomis, “Electrical engineering”

## Slide 30: Three-phase systems
What about a third circuit?
Rull, Galceran, Gomis, “Electrical engineering”

## Slide 31: Three-phase systems
Three-phase system. The common point is called neutral.
=>
Rull, Galceran, Gomis, “Electrical engineering”

## Slide 32: Three-phase systems
Typically, a three-phase system is created by a three-phase generator and not by three different generators.
Rull, Galceran, Gomis, “Electrical engineering”

## Slide 33: Three-phase systems
Three-phase generator
Rull, Galceran, Gomis, “Electrical engineering”

## Slide 34: Three-phase systems
The generator provides a balanced three phase system (the phase-to-neutral voltages are equal).
Rull, Galceran, Gomis, “Electrical engineering”

## Slide 35: Three-phase systems
The nominal voltage of a three-phase system is the line voltage!

## Slide 36: Three-phase systems
Voltages
  Then, we can write the following relations

## Slide 37: Activity IV
Time domain and space representation of three-phase systems
  Create in a Matlab script a three-phase system with the following characteristics: nominal voltage: 400 V (phase-to-phase), nominal frequency: 50 Hz.
    Draw it in the time domain (40 ms)
    Change the following parameters and replot the drawings:
      Frequency
      Amplitude of the phases
      Amplitude of one phase
      Angle of one phase
  Create a three-phase system in Simulink
    Apply the same changes in the time domain.
    Connect the voltage sources to a load and calculate the power for a balanced case.

## Slide 38: Activity IV
  Expected output
Time domain and space representation of three-phase systems

## Slide 39: Activity IV
  Useful tips for scripting
    Write the script in a *.m file
    Write close all, clear all, clc to:
      Close all figures
      Clear all variables
      Clear the command window
    Code selection + F9 – run selected code
    Use two %% to split the code by sections. Run each section with control+Enter
Time domain and space representation of three-phase systems

## Slide 40: Activity IV
Backup code
%% Clear variables&workspace and close windows
clear all; clc; close all;
%% Voltages definition
w = 2*pi*50;
t = 0:0.04/200:0.04;
va = cos(w*t)%+0.1*cos(3*w*t)+0.2*cos(w*t);
vb = cos(w*t - 2*pi/3)%+0.1*cos(3*w*t)+0.2*cos(w*t + 2*pi/3);
vc = cos(w*t + 2*pi/3)%+0.1*cos(3*w*t)+0.2*cos(w*t - 2*pi/3);
%% Plot abc functions
f1 = figure(1);
set(f1, 'Position', [50 500 500 250]);
hold on;
plot(t,va,'LineWidth',1.5,'Color',[0 0 1]);
plot(t,vb,'LineWidth',1.5,'Color',[0 0.6 1]);
plot(t,vc,'LineWidth',1.5,'Color',[0.6 0.6 1]);
l1 = legend('$v_a$','$v_b$','$v_c$');
set(l1,'Interpreter','latex','FontSize',10,'Location','NorthEast');
xlabel('time [s]','Interpreter','latex','FontSize',12);

## Slide 41: Interesting websites
Links
http://stevenblair.github.io/pq/
http://hyperphysics.phy-astr.gsu.edu/hbase/hframe.html